## Slide 1
doc.: IEEE 802.15-22-0652-00-06ma
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) Submission Title: [Soft Spectrum Adaptation(SSA) Based on Pulse Shaping for Interference Mitigation between UWB radio and Other Coexisting Radio]
Date Submitted: [17 November 2022]
Source: [Ryuji Kohno, Takumi Kobayashi] [1;Yokohama National University(YNU), 2;YRP International Alliance Instiitute(YRP-IAI)]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
2; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, Japan 239-0847 ] Voice:[1; +81-90-5408-0611], FAX: [+81-45-383-5528],
Email:[1:kohno@ynu.ac.jp, kobayashi-takumi-ch@ynu.ac.jp, 2:kohno@yrp-iai.jp,]
Abstract: [This document is a copy of the original document “SSA-UWB and Cognitive Radio: a suggestion for global harmonization and compromise in IEEE 802.15.3a WPAN” doc.: IEEE 802.15-04/0253r0 submitted in IEEE802.15.3a May 2004. This Soft Spectrum Adaptation(SSA) technology may be applicable to mitigate interference among IEEE802.15.6ma UWB dependable BAN and other coexisting radio. The SSA can be generally useful in coexistence between UWB radio and other narrow band radio.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)

## Slide 2
doc.: IEEE 802.15-22-0652-00-06ma
Slide 2
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
Soft Spectrum Adaptation(SSA); Synthesizing Pulse Shape Way to Avoid Interference with Coexisting Radios
Ref.[1] H. Zhang, K.Y. Yazdandoost, K.Li, R. Kohno, "SSA-UWB and Cognitive Radio: A Suggestion for Global Harmonization and Compromise in IEEE 802.15.3a WPAN," doc.: IEEE802-15-04-0253-00-003a, May 2004
[2] Ryuji Kohno. Ken-ichi Takizawa, “Soft-Spectrum Adaptation for Detection and Avoidance of UWB
Interference to Existing Radio Systems,” pp.88-91, Frequenz 60 (2006) 5-6

## Slide 3
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [SSA-UWB and Cognitive Radio: a suggestion for global harmonization and compromise in IEEE 802.15.3a WPAN]
Date Submitted: [11 May, 2004]
Source: [Honggang Zhang, Kamya Y. Yazdandoost, Keren Li, Ryuji Kohno ]
Company [ National Institute of Information and Communications Technology (NICT)]
Connector’s Address [3-4, Hikarino-oka, Yokosuka, 239-0847, Japan]
Voice:[+81-468-47-5101], FAX: [+81-468-47-5431],
E-Mail: ［honggang@nict.go.jp, yazdandoost@nict.go.jp, keren@nict.go.jp, kohno@nict.go.jp]
Re: [IEEE P802.15 Alternative PHY Call For Proposals, IEEE P802.15-02/327r7]
Abstract: [In order to realize the global harmonization and compromise in IEEE 802.15.3a UWB WPAN, PSWF-based SSA-UWB systems with improved Common Signaling Mode (CSM) are investigated in NICT and the recent investigation results are briefly summarized. ]
Purpose: [For investigating the characteristics of High Rate Alternative PHY standard in 802.15TG3a, based on the Soft-Spectrum Adaptation (SSA) proposal by NICT.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 4
SSA-UWB and Cognitive Radio:
A Suggestion for Global Harmonization and Compromise in IEEE 802.15.3a WPAN
Honggang ZHANG, Kamya Y. YAZDANDOOST,
Keren LI, Ryuji KOHNO
National Institute of Information and Communications Technology (NICT)

## Slide 5
Outline of presentation
Brief historical retrospect of SSA-UWB PHY proposal
Description of Cognitive Radio (CR) concept
Global harmonization and compromise based on SSA-UWB and Cognitive Radio
 Improved Common Signaling Mode (ICSM) using PSWF-type SSA pulse wavelets
4. Design and implementation of PSWF-type SSA pulse wavelets
5. Conclusion remarks
6. Backup materials

## Slide 6
1. Basic philosophy of Soft-Spectrum Adaptation
Design a proper pulse waveform and code with higher frequency efficiency corresponding to any spectral mask
Adjust transmitted signal’s spectrum with flexibility, so as to minimize interference to/from coexisting systems
Employ optimized pulse wavelet and code to achieve higher system performance

## Slide 7
Modified SSA pulse
Modified SSA pulse
Exchangeable
Power Spectrum
3
1
2
4
5
6
7
8
9
10
11
f
5 GHz
W-LAN
Dual- or three-band
Multi-band or Multi-carrier
Harmonized
with each
through
SSA-UWB pulse wavelet and code
Basic SSA-UWB philosophy (cont.)

## Slide 8
Single-band
Multi-band
In the future, if the restricting ruggedness of regional spectral mask (e.g. FCC mask) is eased, band allocation can be extended below 3.1 GHz or above 10.6 GHz.
Soft-Spectrum Adaptation (SSA) can correspond freely
SSA-UWB with flexible band plan
N division
Power Spectrum
3
1
2
4
5
6
7
8
9
10
11
f [GHz]
5 GHz
W-LAN
Dual- or Triple-band
N+α division

## Slide 9
Features of SSA-UWB
SSA-UWB with flexible pulse waveform, code and frequency band can be applied to single and multi-band/multi-carrier UWB.
Interference avoidance for co-existence, harmonization for various systems, and global implementation can be realized.
 SSA-UWB can flexibly adjust UWB signal spectrum so as to match with any spectral restriction, i.e. spectral masks in both cases of single and multiple bands.
Scalable, adaptive performance improvement.
Smooth system version-up similar to Software Defined Radio (SDR) and Cognitive Radio (CR).

## Slide 10
Soft-Spectrum Adaptation
(SSA)
Geo-
metrical
Free-
verse
Kernel functions
SSA type
Sinusoidal
Multiband with carrier
Multi-carrier
TI
Intel, Wisair
GA, Philips
TF Hopping
TF Coding
Optimized
SSA
Dual-band
Motorola/XSI
Modulated
modified SSA pulse
Adaptive-band
XSI Wavelet
MB-OFDM
Global standard
Gaussian
Adaptive
ST Microelectronics
Mitsubishi
OFDM
Global harmonization and compromise based on SSA-UWB

## Slide 11
2. Improving spectrum usage through Cognitive Radio (CR) technology
“ A Cognitive Radio is a radio frequency transmitter/receiver that is designed to intelligently detect whether a particular segment of the radio spectrum is currently in use, and to jump into (and out of, as necessary) the temporarily-unused spectrum very rapidly, without interfering with the transmissions of other authorized users.”
http://www.ieeeusa.org/forum/POSITIONS/cognitiveradio.html

## Slide 12
At MAC level:
CSMA algorithm
Energy detect channel scan
Active channel scan
Passive channel scan
PAN identifier conflict resolution
Re-transmissions
Dynamic channel selection
At PHY level:
Multi-mode CCA capability
Adjustable TX power
Link quality indication
Examples of Cognitive Radio technology
SSA-UWB is twin of Cognitive Radio

## Slide 13
DS-UWB operating bands
3
4
5
6
7
8
9
10
11
Low Band
3
4
5
6
7
8
9
10
11
High Band
GHz
GHz
MB-OFDM operating bands
3. Improved Common Signaling Mode (ICSM) using PSWF-type SSA pulse wavelets

## Slide 14
Overview of band division and multi-piconets in DS-UWB and MB-OFDM
  DS-UWB has two band group: low band and high band
    2x center frequency and bandwidth in high band
    Support for 6 piconets in each of low band and high band
  MB-OFDM has added full FDM support for multiple piconets using band groups
    New band groups have higher frequencies
    All use same Time-Frequency-Codes (TFC)

## Slide 15: Compatibility and interoperability for multiple modes in a united IEEE 802.15.3a PHY layer
CSM is used for beacon in default mode
CSM can also be used for data exchange in assigned time slots between different class devices (DS-UWB and MB-OFDM)
CSM is designed to be of sufficient data rate to cause minimal impact to super-frame overhead
Beacon
(CSM)
MB-OFDM
Slot
DS-UWB
Slot
Super-frame
CSM
Slot

## Slide 16: Cooperative coexistence and interoperability by Common Signaling Mode (CSM)
Tx
DS-UWB
Rx
DS-UWB
Tx
MB-OFDM
Rx
MB-OFDM

## Slide 17: MB-OFDM & DS-UWB signal spectrum with CSM compromise solution
4488
3960
3432
3100
5100
DS-UWB Low Band
Pulse Shape (RRC)
MB-OFDM (3-bands)
Theoretical Spectrum
Proposed Common
Signaling Mode Band
(500 MHz bandwidth)
FCC Mask
Frequency (MHz)
0
-3
-20
Relative
PSD (dB)
1
2
3
Reference: IEEE 802.15-04/163r0

## Slide 18
Piconet A, IS = {f1,f2,f3,f1,f2,f3,repeat}
Piconet B, IS = {f3,f2,f1,f3,f2,f1,repeat}
Frequency domain spreading (frequency spreading rate ‘2’)
Time-Frequency-Coding in MB-OFDM
A1
(A1)*
B1
(B1)*
A3
(A3)*
B3
(B3)*
A2B2
(A2B2)*
Collision
t
f1
f2
f3
piconetA
piconetB
Reference: IEEE 802.15-03/343r1

## Slide 19
A1
B1
A2
B2
A1B1
Collision
t
f1
f2
f3
A2
B2
A3
B3
A3B3
piconetA
piconetB
Time domain spreading (time spreading rate ‘2’)
Remove conjugate symmetric spreading in frequency domain
200 coded bits per OFDM symbol with each symbol repeated in a different band according to the IS pattern.
Time-Frequency-Coding in MB-OFDM (cont.)
Piconet A, IS = {f1,f2,f3,f1,f2,f3,repeat}
Piconet B, IS = {f3,f2,f1,f3,f2,f1,repeat

## Slide 20
Compatibility and coexistence by improved CSM in a united IEEE 802.15.3a PHY layer
DS-UWB Rx
DS-UWB Tx
MB-OFDM Tx
MB-OFDM Rx
Beacon
(CSM)
MB-OFDM
Time Slot
DS-UWB
Time Slot
Super-frame
CSM
Time Slot
DS-UWB
Time Slot
MB-OFDM
Time Slot

## Slide 21
4488
3960
3432
3100
5100
Frequency (MHz)
0
-3
-20
3.120GHz
572MHz
4.264GHz
572MHz
3.692GHz
4.836GHz
572MHz
572MHz
3.120GHz
572MHz
572MHz
4.836GHz
3.960GHz
Improved Common Signaling Mode based on PSWF-type SSA pulse wavelets
4.836GHz
3.692GHz
3.120GHz
4.264GHz
1
2
3
1+2
2+3
1
3

## Slide 22
Realization of SSA-UWB pulse wavelet design
Not just trying to construct a pulse waveform in order to satisfy the FCC spectral mask, on the contrary, first starting from considering a required spectral mask in frequency domain (band-limited), and then finding its corresponding pulse waveform in time domain (time-limited).
Just as C. E. Shannon has asked a question once upon a time, “To what extent are the functions which confined to a finite bandwidth also concentrated in the time domain? ”, which has given rise to the discovery and usage of Prolate Spheroidal Wave Functions (PSWF) in the sixties.
Designing a time-limited & band-limited pulse waveform is extremely important in UWB system.
Prolate Spheroidal Wave Functions (PSWF)

## Slide 23
Pulse waveforms are doubly orthogonal to each other.
Pulse-width and bandwidth can be simultaneously controlled to match with arbitrary spectral mask adaptively.
Pulse-width can be kept same for all orders of m.
Pulse bandwidth is same for all orders of m.
They can be utilized for simple transceiver implementation since frequency shift, e.g., up-conversion or down-conversion with mixer as in former MB-OFDM and DS-UWB of IEEE 802.15.3a is no longer necessary.
Characteristics of PSWF-based pulse wavelets

## Slide 24
PSWF-type SSA-UWB transceiver achieving Common
Signaling Mode for MB-OFDM and DS-UWB
DS-UWB Rx
DS-UWB Tx
MB-OFDM Tx
MB-OFDM Rx
Frequency-Time-Hopping code with CSM
LNA
Ｘ
Ｘ
Ｘ
Ｘ
Output
Driver
Base
Band
Processor
GCA
GCA
A/D
T/R
SW
Ｘ
Ｘ
Ｘ
Ｘ
PSWF-type SSA pulse bank

## Slide 25
100bits
X
X
X
S/P
S
GI
X
T-H code
IDFT
Interleaver
FEC coding
・・・・・
2bit
QPSK mapping
・・・
QPSK mapping
QPSK mapping
MB-OFDM proposal as reference

## Slide 26
PSWF-type SSA-UWB transceiver achieving Common
Signaling Mode for MB-OFDM and DS-UWB (transmitter)
Binary
Data
１
2
L
S
Interleaver
FEC coding
PSWF-type SSA pulse bank
TFC with CSM

## Slide 27
PSWF-type SSA-UWB transceiver achieving Common
Signaling Mode for MB-OFDM and DS-UWB (receiver)
Binary data
2
1

## Slide 28
Orthogonal PSWF pulse wavelet generation
(3.120-4.264 GHz, order of 1, 2, 3 and 4)

## Slide 29
Orthogonal PSWF pulse wavelet generation
(3.692-4.836 GHz, order of 1, 2, 3 and 4)

## Slide 30
Dual-band PSWF pulse wavelet generation
(3.120-3.692 GHz, 4.264-4.836 GHz)

## Slide 31
4. Design and implementation of PSWF-type SSA pulse wavelets
Effects of UWB antennas on implementation of PSWF-type SSA pulse wavelets

## Slide 32
Orthogonal PSWF-based SSA pulse wavelets (3.1-5.6 GHz, order of 1, 2, 3 and 4)
4.1 Effects of T-type UWB antenna on PSWF pulse wavelets

## Slide 33
Spectral characteristics of PSWF-based SSA pulse wavelets (3.1-5.6 GHz, order of 1, 2, and 3)

## Slide 34
Characteristics of T-type UWB antenna
Frequency (samples)
0
50
100
150
200
250
300
350
400
450
-45
-40
-35
-30
-25
-20
-15
-10
-5
0
Transfer function (S11) characteristics of T-type antenna
Return Loss (dB)
2.32GHz
3.695GHz
5.070GHz
6.44GHz
7.82GHz
9.195GHz
10.57GHz
11.945GHz
T-type UWB antenna designed in NICT

## Slide 35
0
20
40
60
80
100
120
140
-0.14
-0.12
-0.1
-0.08
-0.06
-0.04
-0.02
0
0.02
0.04
0.06
Impulse response of T-type antenna transfer function (S11)
Time (samples)
Relative amplitude
0
50
100
150
200
250
300
350
400
450
-30
-25
-20
-15
-10
-5
0
Phase feature of T-type antenna transfer function (S11)
Frequency (samples)
Relative phase (degree)
Characteristics of T-type UWB antenna (cont.)

## Slide 36
Effects of T-type UWB antenna on orthogonal PSWF pulse shape (order 1)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 37
Effects of T-type UWB antenna on orthogonal PSWF pulse shape (order 2)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 38
Effects of T-type UWB antenna on orthogonal PSWF pulse shape (order 3)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 39
4.2 Effects of K-type UWB antenna on PSWF pulse wavelets
0
20
40
60
80
100
120
140
160
180
-160
-140
-120
-100
-80
-60
-40
-20
0
Phase feature of K-type antenna transfer function (S11)
Frequency (samples)
Relative phase (degree)
0
20
40
60
80
100
120
140
160
180
-25
-20
-15
-10
-5
0
Transfer function (S11) characteristics of K-type antenna
Frequency (samples)
Return Loss (dB)
3.0GHz
3.9GHz
4.9GHz
5.9GHz
6.9GHz
7.9GHz
8.9GHz
9.9GHz
10.9GHz
K-type UWB antenna designed in NICT

## Slide 40
0
20
40
60
80
100
120
140
160
180
-0.08
-0.06
-0.04
-0.02
0
0.02
0.04
0.06
0.08
Impulse response of K-type antenna transfer function (S11)
Time (samples)
Relative amplitude
Impulse response characteristics of K-type UWB antenna

## Slide 41
Effects of K-type UWB antenna on orthogonal PSWF pulse shape (order 1)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 42
Effects of K-type UWB antenna on orthogonal PSWF pulse shape (order 2)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 43
Effects of K-type UWB antenna on orthogonal PSWF pulse shape (order 3)
___ reflected PSWF waveform
___ original PSWF waveform
___ reflected PSWF waveform
___ original PSWF waveform

## Slide 44
4.3 Effects of multipath fading on PSWF pulse wavelets
___ PSWF waveform in fading channel
___ original PSWF waveform
___ in channel
___ original PSWF waveform
___ Rake or Pre-Rake
___ original PSWF waveform

## Slide 45
Effects of multipath fading channel on PSWF pulse wavelets (cont.)
___ Rake or Pre-Rake
___ original PSWF waveform
___ Rake or Pre-Rake
___ original PSWF waveform
___ PSWF waveform in fading channel
___ original PSWF waveform
___ PSWF waveform in fading channel
___ original PSWF waveform

## Slide 46
5. Conclusion remarks
A combined SSA-UWB and Cognitive Radio scheme has been suggested for global harmonization and compromise in IEEE 802.15.3a, based on Common Signaling Mode with PSWF-type pulse wavelets.
We also have investigated the effects of two specific Ultra Wideband antennas on the implementation issue of PSWF-type pulse wavelets.
 Measurement and simulation results are very encouraging as well.
Scalable and adaptive performance improvement with multi-mode (DS-UWB & MB-OFDM) can be further expected by utilizing the PSWF-based SSA-UWB and Cognitive Radio.

## Slide 47
6. Background materials

## Slide 48
Design PSWF-based SSA pulse wavelets
N division

## Slide 49
Realization of SSA-UWB pulse wavelet design
Not just trying to construct a pulse waveform in order to satisfy the FCC spectral mask, on the contrary, first starting from considering a required spectral mask in frequency domain (band-limited), and then finding its corresponding pulse waveform in time domain (time-limited).
Just as C. E. Shannon has asked a question once upon a time, “To what extent are the functions which confined to a finite bandwidth also concentrated in the time domain?”, which has given rise to the discovery and usage of Prolate Spheroidal Wave Functions (PSWF) in the sixties.
Designing a time-limited & band-limited pulse waveform is extremely important in UWB system.
Prolate Spheroidal Wave Functions (PSWF)

## Slide 50
Designing method of optimized SSA-UWB wavelets using PSWF
Power Spectrum
3
1
2
4
5
6
7
8
9
10
11
f [GHz]
5 GHz
W-LAN

## Slide 51
Designing method of optimized SSA-UWB wavelets using PSWF (cont.)

## Slide 52
What’s Prolate Spheroidal Wave Functions (PSWF)?

## Slide 53
Pulse waveforms are doubly orthogonal to each other.
Pulse-width and bandwidth can be simultaneously controlled to match with arbitrary spectral mask adaptively.
Pulse-width can be kept same for all orders of m.
Pulse bandwidth is same for all orders of m.
They can be utilized for simple transceiver implementation since frequency shift, e.g., up-conversion or down-conversion with mixer as in MB-OFDM and DS-UWB of IEEE 802.15.3a is no longer necessary.
Characteristics of PSWF-based pulse wavelets

## Slide 54
Numerical solution of PSWF

## Slide 55
Discrete-time solution of Prolate Spheroidal Wave Functions (PSWF) with eigenvalue decomposition
Numerical solution of PSWF (cont.)

## Slide 56
-5
-4
-3
-2
-1
0
1
2
3
4
5
x 10
-10
-0.4
-0.3
-0.2
-0.1
0
0.1
0.2
0.3
0.4
Optimized pulse waveform generation based on PSWF
Time (sec)
Relative Amplitude
____ order of 1
_ _ _ order of 2
........ order of 3
Power Spectrum
3
1
2
4
5
6
7
8
9
10
11
f [GHz]
5 GHz
W-LAN
Orthogonal pulse waveform generation based on PSWF (3.1-10.6 GHz, order of 1, 2 and 3).

## Slide 57
Orthogonal pulse waveform generation based on PSWF (3.1-5.6 GHz, order of 1, 2, 3 and 4).
-1.5
-1
-0.5
0
0.5
1
1.5
x 10
-9
-0.4
-0.3
-0.2
-0.1
0
0.1
0.2
0.3
0.4
Optimized pulse waveform generation based on PSWF
Time (second)
Relative Amplitude
___ order of 1
…... order of 2
-1.5
-1
-0.5
0
0.5
1
1.5
x 10
-9
-0.4
-0.3
-0.2
-0.1
0
0.1
0.2
0.3
Optimized pulse waveform generation based on PSWF
Time (second)
Relative Amplitude
___ order of 3
…... order of 4

## Slide 58
doc.: IEEE 802.15-22-0652-00-06ma
Slide 58
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
7. Conclusion
Soft Spectrum Adaptation(SSA) for UWB pulse shaping is a general technology to avoid interference between a UWB radio such as UWB WPAN of IEEE802.15 and a narrow band radio such as WLAN of IEEE802.11, WiFi, BT, BLE etc.
SSA can be applied for a UWB pulse shape so as to be matched with spectrum mask in radio regulation.