## Slide 1: MAC address assignment in IEEE 802.11 through IEEE 802.11aq
Antonio de la Oliva (UC3M, IDCC)
aoliva@it.uc3m.es
Robert Gazda (IDCC)
robert.gazda@interdigital.com

## Slide 2: IEEE 802.1CQ Scope
As defined in the PAR:
“This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses to ports in IEEE 802 networks”
Actually, we are working on mechanisms for the distribution of Local MAC addresses (in the 802c defined SAI space) including stateful and stateless procedures, on a per-technology basis.

## Slide 3: Scenarios
Functional Scenarios
  Stateless/Statefull Assignment of addresses to End-stations
    802.11
    802.3
    VMs/Containers
    802.15 (if expertise appears)
  Stateless/Statefull Assignment of addresses to Bridges/APs
    Including Assignment of groups of addresses
  Statefull Assignment of pools of addresses to Proxies from Servers
Network Scenario
  Hypervisor scenario
  Container scenario
  WLAN scenario

## Slide 4: Motivation for a specific mechanism in IEEE 802.11
MAC address is part of the state information required for the association and security in WLAN
  Any modification of MAC address in WLAN forces a new association and security association establishment
If MAC assignments are required in a given network, it is required to discover the address in pre-association

## Slide 5: Proposal
Use IEEE 802.11aq mechanisms to discover LAAP services and provide MAC address assignment in pre-Discovery state
  Use of Service Hint/Hash to advertise LAAP service
  Use new protocol within Service Information Request/Response Element in IEEE 802.11aq modified ANQP to negotiate MAC address

## Slide 6: Service Advertisement
IEEE 802.11aq defines two mechanisms for the distribution of information about services available
  Service Hint: The Service Hint element provides a probabilistic representation of a set of services that are available to the BSS (Bloom filter).
  Service Hash: The Service Hash element contains one or more service hashes.
How to compute both is defined in Clauses 11.25a.4 and 11.25a.5 of IEEE 802.11aq
Proposal:
  Define the following service names following RFC6335
    Ieee-8021cq-LAAP-server
    Ieee-8021cq-Self-Assignment
    Ieee-8021cq-Self-Assignment-with-prefix
    Ieee-8021cq-LAAP-server-optional
  PAD-enabled STA will advertise the above services when available

## Slide 7: Exchanging messages with the LAAP Proxy ServerArquitecture

## Slide 8: Exchanging messages with the LAAP Proxy ServerProcedure (.11aq compatible)
And here you have a last step, association

## Slide 9: Exchanging messages with the LAAP Proxy ServerProtocol
Need to define a new protocol on top of Service Information Request/Response Element
Value | Description
0 | Request
1 | Rebind
2 | Response
3-255 | Reserved

## Slide 10: Conclusion
Pre-association Discovery in WLAN can be done through the use of IEEE 802.11aq
802.1CQ can be in charge of defining the new service names and registering them in IANA
802.1CQ can design the protocol on top of 802.11aq ANQP extensions (Service Information Request Response) to assign MAC addresses
This will not require of any change to IEEE 802.11